Scientific requirements and dimensioning for the MICADO-SCAO RTC

---
Global overview of the instrument
Shown in ‘stand-alone’ phase.
Same mount structure as when under MAORY.
Design spaces:
Fold mirror & calibration unit
SCAO
(+ MAORY NGS-WFS)
Cryostat & derotator
Electronics (co-rotating)
Cable-wrap

---
SCAO performance
Based on end-to-end GPU simulations
Maximum strehl
Limited by M4 and telescope WFE budget
Residual tip-tilt ~3mas
Anisoplanatism
Different to 8-m telescopes, because E-ELT diameter is comparable to L0.
Although strehl ratio is low, PSF retains a diffraction limited core even far off-axis
PSF with radial & transverse cuts, 30” off-axis, for realistic L0 profile
(K-band Strehl ~6%)
(Clénet+ 13, 14)

---
MICADO SCAO in few numbers
- MICADO-SCAO
  - Framerate : 1000Hz
  - 1 SH WFS :
    - 840x840 pixels @1kHz ~11.3Gb/s
    - 80x80 ssp, let say ~10k measurements
  - 1 DM : ~5k commands
  - Command matrix : ~50Mb

---
MICADO-SCAO RTC
- Hard real-time subsystem:
  - Baseline, linear control with matrix-vector multiply
  - MVM Performance : 100 Gflops
  - Determinism : 10% jitter over a 1000 FPS framerate : 100µs requirement
  - Technology trade off study : CPU / GPU / FPGA
- Supervision module : optimization of hard-real time parameters
  - Main task : regular control matrix update
  - SVD Performance : 750Gflop (but memory-bound)
  - Addressed with a standard HPC cluster

---
GPU Compute performance
- For the computation part, 1 GPU is enough :
- But, MVM is a io bound problem, the memory bandwidth the first performance indicator.
  - NGPU = CEIL( CR / (B * FPP) ) = 2 GPUs K40
    100 Gflops / (1880 Mb/s * 32) = 1.7
Model	Architecture	Theoretical peak performance single precision (TFLOPS)	Memory bandwidth (Gb/s)	ECC	Energy consumption (W)
NVidia Tesla K40	Kepler	4.29	2304	Yes	235
NVidia Tesla K80	Kepler	8.5	3840	Yes	300
NVidia M6000	Maxwell	6.07	2539	No	222
	K20C	K40	K80	M6000
B theo	1664	2304	1920 (x2)	2539
B ECC off	1400 (84%)	1888 (82%)	1536 (x2, 80%)	1968 (77%)
B ECC on	1200 (72%)	1664 (72%)	1360 (x2, 70%)	NONE

---
GPU Compute performance
- Need for tailored data acquisition process
- See Denis Perret & Julien Bernard presentations tomorrow

---
CPU Compute performance
- Intel Xeon CPU / Xeon Phi
  - Between 100 & 280 GB/s memory bandwidth per processing units
  - Up to 5 CPUs or 2 Xeon Phis (see David Barr presentation tomorrow)
- Reference solution using standard libraries and portable code
- Need vectorization on Xeon Phi to meet peak performance
- Long term availability of Xeon Phis questionable

---
FPGA Compute performance
- ARRIA 10AS066 SoC
  - 1.5GHz ARM dual-core Cortex-A9 co-processor
  - 1855 DSP blocks
  - 5.2MB int. RAM
  - max. 48 XCVR links
- ARRIA 10AX115
  - 1518 DSP blocks
  - 6.6MB int. RAM
  - max. 96 XCVR
- 40 GMAC/s peak performance (80 GFLOP/s)
  - 2 boards are needed to meet performance specifications

---
ESO specific constraints
- ESO is gathering instrument specifications to build a standardized AO RTC approach (SPARTA evolution ?)
- ESO will define a RTC toolkit for instrument consortia
- Need to take into account E-ELT specificities : e.g. M4 control, handover between telescope control system and AO system …
- Instrument calibration issues : limited daytime slots for instrument calibration may impose efficient strategies with strong computing constraints

---
Conclusions
- MICADO Preliminary Design Phase has started
- Dimensioning a RTC for the SCAO mode
- Will lead trade off studies for RTC technologies down selection
- Interaction with ESO needed to be compliant with RTC toolkit and design full RTC pipeline including M4 control / interaction with telescope
- Output of Green Flash project (Damien Gratadour presentation) critical for design consideration