## Slide 1: IBM Power system – HPC solution
Real-time control for adaptive optics workshop
26-27 January 2016
Guillaume Villette (guillaume.villette@fr.ibm.com)

## Slide 2: IBM Power system HPC ecosystem Applications
AGENDA:

## Slide 3
Power system – An OpenPOWER initiative
Moore’s law no longer satisfies performance gain
Growing workload demands
Numerous IT consumption models
Mature Open software ecosystem
Rich software ecosystem
Spectrum of power servers
Multiple hardware options
Derivative POWER chips
OpenPOWER is an open development community, using the POWER Architecture to serve the evolving needs of customers.
Performance of POWER architecture
amplified capability
Open Development
open oftware, open hardware
Collaboration of thought leaders
simultaneous innovation, multiple disciplines
Feeds back … resulting in client choice

## Slide 4
Power system – An OpenPOWER initiative
GPU
NVLINK
Memory
DMI
FPGA
CAPI/PCIe

## Slide 5
Power8 chip
Core
L2
Core
L2
Core
L2
Core
L2
Core
L2
Core
L2
Core
L2
Core
L2
Core
L2
Core
L2
Core
L2
Core
L2
L3 Cache & Chip Interconnect
8M L3
Region
Mem. Ctrl.
Mem. Ctrl.
SMP Links
Accelerators
SMP Links
PCIe
Bus Interfaces
Integrated PCIe Gen3
SMP Interconnect
CAPI
Accelerators
Crypto & Random number generator
Transactional Memory & Active memory expansion
Data Move / VM Mobility
Caches
64K Data cache (L1)
512 KB SRAM L2 / core
96 MB eDRAM shared L3
Up to 128 MB eDRAM L4 (off-chip)
Cores
10-12 cores (SMT8)
8 dispatch, 10 issue, 16 exec pipe
2X internal data flows/queues
Enhanced prefetching
Memory
Dual memory Controllers
230 GB/sec Sustained bandwidth
Technology
22nm SOI, eDRAM, 15 ML 650mm2

## Slide 6: GPU - NVLink
NVIDIA GPU
NVIDIA GPU with NVLink
Current GPU Attach
Power Chip
with NVLink
80 GB/s
Peak*
Graphics Memory
Graphics Memory
System Memory
40+40 GB/s
40+40 GB/s
40+40 GB/s
Power Chip
PCIe x16
Graphics Memory
System Memory
16+16 GB/s
“NVLink will help improve GPU-GPU peer-to-peer communications, eliminating the need to transfer data via the PCIe bus. It would also allow one or more GPUs to access the system RAM much quicker. The new protocol will debut in 2016 with Pascal, which was revealed to be NVidia's next GPU architecture.”
Future NVLink GPU Attachment

## Slide 7: CAPI – Coherent Accelerator Processor Interface
POWER8 Core
CAPP
PCIe
POWER8 Processor
OS
App
Memory (Coherent)
FPGA
AFU
IBM Supplied PSL
Typical I/O Model Flow:
Flow with a Coherent Model:
Shared Mem.
Notify Accelerator
Acceleration
Shared Memory
Completion
DD Call
Copy or Pin
Source Data
MMIO Notify
Accelerator
Acceleration
Poll / Interrupt
Completion
Copy or Unpin
Result Data
Ret. From DD
Completion
Application
Dependent, but
Equal to below
Application
Dependent, but
Equal to above
300 Instructions
10,000 Instructions
3,000 Instructions
1,000 Instructions
1,000 Instructions
7.9µs
4.9µs
Total ~13µs for data prep
400 Instructions
100 Instructions
0.3µs
0.06µs
Total 0.36µs

## Slide 8: IBM OpenPOWER – Based HPC Roadmap
2015
2016
2017
Connect-IB
FDR (50Gb/s)
PCIe Gen3
ConnectX-4
EDR (100Gb/s)
CAPI over PCIe Gen3
ConnectX-5
HDR (200Gb/s)
Enhanced CAPI over
PCIe Gen4
Mellanox
Interconnect Technology
IBM CPUs
NVIDIA GPUs
Tesla
PCIe Gen3
Volta
Enhanced NVLink
Pascal
NVLink
POWER8
OpenPower
CAPI Interface
POWER8
NVLink
POWER9
Enhanced CAPI & NVLink
Compilers
XL
LLVM – OpenMP4 (C)
GCC – OpenACC 1+
XL
LLVM – OpenMP 4.1
GCC – OpenACC 2
PGI – OpenACC 2
XL – OpenMP 5
LLVM – OpenMP 5
GCC – OpenACC
PGI – OpenACC 3
Libraries
ESSL/PESSL
MASS
PE
ESSL/PESSL + GPU
MASS
Plateform MPI
ESSL/PESSL + GPU
MASS
Plateform MPI

## Slide 9: IBM HPC ecosystem - Platform Computing
IBM Platform Computing
RTM
LSF
PAC
Spectrum Scale/ ESS
Platform Clustering Manager
xcat
Provisioning
Storage
Resource
Management

## Slide 10: Applications considered
# Applications Application Category | Ported | GPU Enabled | Performance Metrics Avail | In-process | Planned to be ported | Under Consideration
Astrophysics | 2 | 2 | 2 | 0 | 3 | 2
Biological Sciences | 55 | 9 | 4 | 2 | 14 | 15
Chemistry and Physics | 7 | 4 | 3 | 12 | 16 | 37
Computer-aided Engineering (CAE) | 8 | 3 | 3 | 0 | 5 | 4
Deep Learning | 0 | 0 | 0 | 1 | 0 | 3
Defense & Intelligence | 0 | 0 | 0 | 0 | 0 | 0
Digital Content Creation and Distribution (DCC / DCD) | 0 | 0 | 0 | 0 | 0 | 0
Electronic Design Automation (EDA) | 1 | 0 | 1 | 0 | 0 | 0
Financial Modeling | 5 | 2 | 2 | 0 | 0 | 5
Geosciences | 2 | 1 | 1 | 1 | 7 | 13
Weather and Climate | 8 | 1 | 1 | 1 | 5 | 10
Benchmarks | 11 | 6 | 5 | 1 | 5 | 1
Utilities | 15 | 9 | 0 | 4 | 2 | 6

## Slide 11: Applications considered
Chart: Relative Performance
| Ludwig | Gadget | VASP: TC3 | ALYA: Cavity | BWA | VASP: TC2 | NAMD: apoa1 | CPMD:Large | NAMD: STMV | EDA Throughput | Saturne | FSS STAC-A2 | RTM
Haswell | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
POWER8 | 0.93 | 0.96 | 0.96 | 1.06 | 1.1 | 1.12 | 1.42 | 1.43 | 1.51 | 1.53 | 1.88 | 2.3 | 2.6
POWER8: Application Performance Advantages over Intel Haswell

## Slide 12: Questions? guillaume.villette@fr.ibm.com